## Slide 1
AI-Based Construction Safety Inspection and Compliance
Nithin H – 1RVU23CSE314
Panav Kumar K – 1RVU23CSE331
Pranav Nayak – 1RVU23CSE344
Desu Sree Vardhan – 1RUA24CSE7004
Mid-review video presentation

## Slide 2
How the presentation is organised
One connected argument split across four speakers, roughly five minutes each.
Speaker | Section | What it covers
1 | Why computer vision first | Motivation, precise problem statement, the CV pipeline, and the incident record it produces
2 | PPE and detection literature | Six papers on construction PPE detection and the YOLO detector family, then what detection alone cannot do
3 | Tracking and activity literature | Six papers on multi-object tracking, harness detection and construction activity recognition
4 | Multimodal models and evaluation | Three papers on vision-language models, the research gaps, our evaluation plan and scope

## Slide 3
CCTV is already everywhere, but safety review is still reactive
The footage exists. What is missing is anything that turns it into a decision.
THE SITUATION ON SITE
• A large site has hundreds of workers and moving plant, supervised by a handful of safety officers
• Cameras are already installed almost everywhere, so the video exists, but nobody can watch it live
• Review usually happens after an accident, when footage becomes evidence rather than prevention
WHY A BARE ALERT IS NOT ENOUGH
• Helmet missing does not say which worker, or for how long
• It carries no image, so the call cannot be verified or disputed
• It repeats every frame, so one violation becomes hundreds of alerts
• With no record there is nothing to audit, assign or close out
WHAT A SAFETY OFFICER ACTUALLY NEEDS
• A specific worker, a time range, and the named rule that was broken
• The evidence crop that triggered it, so the call can be checked
• An honest uncertainty state when the camera simply could not see
• A plain explanation of why it matters and what to do next

## Slide 4
Problem statement: from raw video to reviewable incidents
Stated as one sentence, then broken into what must be seen and what must be reasoned.
PRECISE STATEMENT
• Build a video-analysis system that takes pre-recorded construction footage, detects safety hazards, tracks the worker involved, classifies the PPE evidence, and emits incident records carrying rule, severity, duration and an evidence crop.
WHAT MUST BE PERCEIVED
• Workers, and whether each wears a helmet and a high-visibility vest
• Machinery and plant, so worker-to-equipment proximity can be measured
• Restricted zones and elevated edges, defined once on the site plan
WHAT MUST BE REASONED ABOUT
• Identity across frames, so one worker is not counted as many
• Duration, so a brief pass-through is not treated as sustained breach
• Uncertainty, so an unreadable crop is marked unknown, not guessed
WHAT MUST BE PRODUCED
• A record with worker, rule, time range, location and evidence
• A confirmed or inconclusive status that is never silently upgraded
• Output stable enough for a later model to explain without re-deciding
EXPLICITLY NOT THE PROBLEM
• Live real-time monitoring of an operating site
• Deciding legal liability or issuing a regulatory verdict
• Replacing the safety officer's judgement with a model's opinion

## Slide 5
Computer vision decides; the language model only explains
This boundary is what keeps the project a safety tool rather than a chatbot over footage.
COMPUTER VISION OWNS THE EVIDENCE
• Worker identity, time range, rule fired, location and image crop all come from detection, tracking and the rule engine
• Every field is reproducible: the same clip yields the same record
• Confidence values are stored alongside the verdict, not hidden
THE LANGUAGE MODEL COMES AFTERWARDS
• It writes the explanation, drafts the briefing and answers questions
• It reads only the structured fields the pipeline already produced
• It cannot create, delete or change a safety verdict
WHY THE ORDER MATTERS
• A model that both detects and explains cannot be audited: there is no independent record to check its story against
• Separating them means a wrong explanation is visibly wrong
• It also lets us evaluate perception and language separately
HANDLING WEAK EVIDENCE
• When the crop is occluded or too small, PPE state is recorded as unknown
• The incident is reported inconclusive rather than asserted
• A vision model may be asked to adjudicate, but the rule still decides

## Slide 6
Proposed computer vision pipeline
Six stages run before any language model is involved.
Each stage answers one question: what is in the frame, who it is over time, what they are wearing, and whether that combination breaks a rule. Nothing downstream can override an earlier stage, so every incident traces back to a specific frame and box.

## Slide 7
The output: a structured incident record
Whenever later slides say incident, this is the object being described.
Field | Example value | Where it comes from
Worker | Track 17 | ByteTrack identity, persistent across the clip
Rule | R1 - helmet required | Rule engine, evaluated over a time window
Severity | High | Fixed severity attached to the rule, not inferred
Time | 00:41.2 to 00:45.5 (4.3 s) | Track start and end, after debounce
Location | Zone B, near elevated edge | Worker box against the annotated site plan
Evidence | Cropped frame at 00:43.0 | Highest-confidence frame in the window
Confidence | detector 0.88 / PPE 0.71 | Raw model scores, stored unrounded
Status | Confirmed | Becomes inconclusive if PPE state is unknown
Every field is produced by the CV pipeline and the rule engine. The language model reads this record; it never writes to it.

## Slide 8
Literature survey: 15 original papers reviewed
One-slide overview before the individual paper discussion.
Paper | Focus | One-line relevance
Nath et al. 2020 | PPE detection | detect-then-classify PPE baseline for site images
Wu et al. 2019 | Hardhat detection | small-object hardhat detection and colour classes
Fang et al. 2018 | CV safety survey | maps CV safety gaps: alerts, uncertainty, action
Redmon and Farhadi 2018 | YOLOv3 | real-time single-stage detector baseline
Bochkovskiy et al. 2020 | YOLOv4 | speed-accuracy improvements on modest hardware
Wang et al. 2024 | YOLOv9 | modern YOLO reference for efficient detection
Zhang et al. 2022 | ByteTrack | tracks workers by associating every detection box
Aharon et al. 2022 | BoT-SORT | fallback tracker using motion plus appearance
Wojke et al. 2017 | DeepSORT | classic appearance-based tracking baseline
Fang et al. 2018b | Harness detection | fall-risk PPE checking at elevated work areas
Sanhudo et al. 2021 | Activity recognition | time-windowed worker activity classification
Luo et al. 2018 | Site activity images | uses scene/object context for activity labels
Achiam et al. 2023 | GPT-4 | vision-language reasoning, used only after CV uncertainty
Liu et al. 2023 | LLaVA | open visual question-answering baseline
Yang et al. 2024 | Qwen2.5 | small open LLM for grounded incident narration

## Slide 9
Nath et al. 2020
Deep learning for site safety: real-time detection of protective equipment | PPE detection
METHOD
• YOLO-based detector trained on a crowdsourced construction image dataset
• Compares three strategies: detect PPE items directly, detect combined worker-plus-PPE classes, or detect the worker then classify the crop
• The combined-class approach reached the best mean average precision of 72.3 percent
• The third strategy pairs a worker detector with a separate CNN classifier per crop
CONTRIBUTION
• Demonstrates PPE compliance checking on genuine site imagery, not staged photos
• Shows classifying a cropped worker beats detecting small PPE items directly
• Publishes construction-specific labels instead of reusing generic object classes
• Establishes the accuracy range a student-scale PPE system can realistically hit
LIMITATION
• Output is a per-frame compliance label with no worker identity or duration
• Covers helmet and vest only, with no reasoning about occlusion or camera angle
• A fixed-label classifier must still pick a class when the helmet is not visible
HOW WE USE IT
• Validates our detect-then-classify design: YOLO finds the worker, a second head reads PPE from the crop
• We keep their crop-classifier idea but add an explicit unknown state for poor visibility
• Their reported accuracy gives us a realistic target for our own detection metric

## Slide 10
Wu et al. 2019
Automatic detection of hardhats worn by construction personnel | Hardhat detection
METHOD
• Single-shot detector with an attention mechanism aimed at small objects
• Introduces a benchmark of site images labelled by hardhat colour
• Detects five classes: no-hardhat plus blue, white, yellow and red hardhats
• Uses a lightweight backbone chosen for practical on-site deployment
CONTRIBUTION
• Confirms helmet status is readable from CCTV-resolution imagery
• Colour classes let a system separate roles such as visitor, worker and supervisor
• Shows attention on shallow layers measurably improves small-object recall
• Provides a reusable public benchmark for hardhat detection
LIMITATION
• Helmet only, so a worker missing a vest or standing in a restricted zone is invisible
• Per-image detection with no tracking, so one violation recounts on every frame
• Produces a box on a frame rather than a record of what happened
HOW WE USE IT
• Supports rule R1 on mandatory helmets and flags small-object recall as a real risk
• Shows why our scope must cover vest and zone rules, not hardhats alone
• Their colour classes are a candidate later extension for role-aware rules

## Slide 11
Fang et al. 2018
Computer vision applications in construction safety assurance | Survey
METHOD
• Reviews computer vision work across detection, tracking and behaviour analysis
• Groups applications by hazard: falls, PPE non-compliance, equipment proximity, unsafe acts
• Compares handcrafted-feature methods against early deep learning approaches
• Catalogues the datasets and evaluation practices in use across the field
CONTRIBUTION
• Establishes vision-based safety assurance as a legitimate, active research area
• Identifies that most systems stop at detection and never close the loop to action
• Highlights the absence of shared construction-specific benchmarks
• Gives a shared vocabulary for hazard types that we adopt for our rules
LIMITATION
• Surveyed systems emit alerts, not records a safety officer can review and act on
• Almost no attention to uncertainty, occlusion, or explaining a decision
• Little work links a detected hazard to a regulation or a required response
HOW WE USE IT
• This survey defines our central gap: move from a raw alert to a usable incident
• Its hazard taxonomy maps almost directly onto our rules R1 to R5
• Its note on missing explanations is what justifies our LLM briefing layer

## Slide 12
Redmon and Farhadi 2018
YOLOv3: An Incremental Improvement | Object detection
METHOD
• Single-stage detector predicting boxes, objectness and classes in one forward pass
• Darknet-53 backbone predicting at three scales to cover different object sizes
• Independent per-class logistic classifiers instead of a softmax over classes
• Trained at several input resolutions to trade speed against accuracy
CONTRIBUTION
• Made real-time detection practical on a single GPU at usable accuracy
• Three-scale prediction substantially improved small-object detection
• Became the baseline that the construction-safety papers above are built on
• Its architecture is still the reference point every later tracker assumes
LIMITATION
• A general-purpose detector with no notion of who a person is between frames
• No temporal reasoning, so it cannot express duration or persistence
• Trained on generic classes; helmets and vests are not in its vocabulary
HOW WE USE IT
• Justifies a single-stage YOLO detector as the first stage of our pipeline
• Its multi-scale design matters because workers are small in wide CCTV views
• Shows we must fine-tune on construction data rather than use pretrained weights

## Slide 13
Detection literature gives us boxes, not incidents
Closing the six PPE and detection papers: what is solved, and what is still open.
WHAT THESE SIX PAPERS SETTLE
• PPE is visually detectable at CCTV resolution, on real site imagery
• Detect-then-classify beats detecting small PPE items directly
• Single-stage detectors are fast and accurate enough on one GPU
• Detection quality depends far more on training data than architecture
WHAT THEY LEAVE UNSOLVED
• Every one of them outputs a per-frame label or box, never a record
• None carries worker identity, so duration cannot be expressed
• None has an uncertainty state; the classifier must always pick a class
• None connects a detection to a rule, a severity or a required action
WHAT WE THEREFORE BUILD ON TOP
• Take the YOLO detector and crop-classifier pattern as given, then add the three missing pieces: a tracker for identity and duration, an explicit unknown PPE state, and a rule engine that turns a sustained condition into an incident record

## Slide 14
Zhang et al. 2022
ByteTrack: Multi-Object Tracking by Associating Every Detection Box | Tracking
METHOD
• Associates every detection box with tracks in two stages, including weak ones
• High-confidence boxes match first using Kalman motion prediction and box overlap
• Remaining low-confidence boxes then match unmatched tracks to recover occlusions
• Deliberately uses no appearance embedding, which keeps the tracker cheap
CONTRIBUTION
• Reaches 80.3 MOTA and 77.3 IDF1 on MOT17 at around 30 frames per second
• Shows most tracking failures come from discarding low-confidence detections
• Simple enough to implement, debug and explain inside a semester project
• Needs no extra model to train, which keeps our pipeline auditable
LIMITATION
• Assumes a reasonably stable camera and can still switch identities in dense crowds
• Without appearance features it cannot re-identify a worker who leaves and returns
• Tracking quality is capped by detector quality on the same frames
HOW WE USE IT
• Our primary tracker, giving each worker an identity that persists across the clip
• Turns a bare alert into worker 17 was uncovered for 4.3 seconds
• Its weak-box recovery is exactly what we need when workers pass behind scaffolding

## Slide 15
Fang et al. 2018b
Falls from heights: computer vision based safety harness detection | Construction safety
METHOD
• Two-stage pipeline: a detector locates workers, a second network checks for a harness
• Targets workers operating at height, where fall protection is mandatory
• Trained on site images of scaffolding and structural steel work
• Reports precision and recall for harness presence, not only detection accuracy
CONTRIBUTION
• Shows vision can target the highest-consequence hazard class, falls from height
• Validates a detect-then-verify pattern for a specific safety attribute
• Demonstrates a context-dependent rule: the harness only matters when at height
• Reports attribute-level precision and recall, which is how we will score PPE
LIMITATION
• Judges each frame independently, with no duration or persistence requirement
• Harness straps are thin and frequently occluded, which limits reliability
• Does not determine elevation automatically from the scene
HOW WE USE IT
• Directly supports rule R5 on elevated edges and fall risk
• Confirms our two-stage detect-then-classify structure for PPE attributes
• Its context dependence is why our rules combine PPE state with zone information

## Slide 16
Sanhudo et al. 2021
Activity classification of construction workers | Activity recognition
METHOD
• Classifies worker activity from wearable accelerometer signals
• Compares several classifiers over features extracted from signal windows
• Focuses on labour-intensive tasks relevant to ergonomic and safety risk
• Uses time-windowed features rather than instantaneous readings
CONTRIBUTION
• Shows worker behaviour is machine-recognisable into meaningful categories
• Time-windowed classification is markedly more reliable than per-instant labels
• Links activity recognition to safety outcomes, not only productivity
• Confirms activity categories are stable enough to be worth detecting at all
LIMITATION
• Sensor-based, so every worker must wear and maintain a device
• Produces no visual evidence, so a supervisor cannot verify the classification
• Does not scale to a site that already has cameras but no wearables
HOW WE USE IT
• Reinforces our choice of time windows over per-frame labels in the rule engine
• Its lack of visual evidence is why our incident cards must carry an image crop
• Motivates deriving activity context from video rather than from extra hardware

## Slide 17
Luo et al. 2018
Recognising diverse construction activities in site images | Activity recognition
METHOD
• A relevance network relates detected objects to candidate activity classes
• Handles many activity classes in cluttered, unconstrained site photographs
• Uses object co-occurrence as evidence rather than whole-image features
• Evaluated across a wide range of real construction activity categories
CONTRIBUTION
• Demonstrates activity recognition works on genuinely messy site imagery
• Object-relation reasoning generalises better than whole-image classification
• Establishes that context, not just the worker, decides whether a scene is unsafe
• Shows a model can use the scene, not just the person, as safety evidence
LIMITATION
• Per-image classification with no tracking, so it cannot measure how long anything lasted
• Cannot separate a worker passing through a zone from one working inside it
• No mechanism to express uncertainty when the scene is ambiguous
HOW WE USE IT
• Its per-frame limitation is the clearest argument for our track-first design
• Its object-relation idea informs how we compute worker-to-zone relations
• Confirms that a single frame cannot support a defensible safety verdict

## Slide 18
Safety rules need time, identity and context
Closing the six tracking and activity papers: why one frame is never enough.
WHAT TRACKING CONTRIBUTES
• A stable identity, so the same worker is one subject and not many alerts
• A measurable duration, which is what separates a breach from a pass-through
• Recovery through occlusion, which is constant on a cluttered site
• A ranked set of frames, so we can pick the clearest evidence crop
WHAT THE ACTIVITY PAPERS WARN US ABOUT
• Site scenes are cluttered, varied and hard to label from one image
• Context decides risk: the same posture is safe or unsafe by location
• Per-frame classifiers cannot express how long a state persisted
• Sensor-based methods work but leave no evidence a supervisor can check
HOW OUR RULE ENGINE RESPONDS
• Rules R1 to R5 take a tracked worker, a PPE state and a zone relation, then require the condition to hold for a minimum duration before firing, with debouncing so flicker does not create duplicate incidents

## Slide 19
Achiam et al. 2023
METHOD
• Transformer model accepting interleaved image and text input and producing text
• Post-trained with reinforcement learning from human feedback for instruction following
• Evaluated on academic and professional exams alongside standard benchmarks
• Reports a dedicated safety and refusal evaluation beside the capability numbers
CONTRIBUTION
• Shows one model can describe and reason about image content in plain language
• Strong instruction following makes format-controlled output practical
• Its documented refusal behaviour is a usable building block for a safety product
• Sets the expectation that a visual explanation can read as genuinely useful
LIMITATION
• Closed weights behind an external API, so evidence crops leave our infrastructure
• Still invents confident detail that is not present in the image
• Gives no calibrated confidence, so its judgement cannot serve as a verdict
HOW WE USE IT
• Supports calling a vision model only to adjudicate cases our pipeline marks unknown
• Its hallucination risk is why the LLM never overrides a rule outcome in our design
• Its refusal work backs our guardrail that declines legal-verdict questions

## Slide 20
Liu et al. 2023
Visual Instruction Tuning (LLaVA) | Vision-language model
METHOD
• Connects a frozen vision encoder to a language model through a projection layer
• Trained on machine-generated multimodal instruction-following data
• Two stages: align the projection first, then instruction-tune end to end
• Evaluated on visual question answering and open-ended visual conversation
CONTRIBUTION
• Open-weight proof that visual question answering can run on self-hosted hardware
• Shows synthetic instruction data is enough to teach visual conversation cheaply
• Gives a reproducible reference architecture we could realistically deploy
• Removes any dependency on a paid API for the explanation layer
LIMITATION
• Not construction-specific and untested on low-resolution CCTV crops
• Weaker than closed models on fine detail such as a partly hidden strap
• Ungrounded by default; it answers even with no supporting visual evidence
HOW WE USE IT
• Our open-weight option if evidence crops cannot be sent to an external API
• Its grounding weakness motivates an overlap check between answer and evidence
• Baseline for the idea of explaining an evidence crop in plain language

## Slide 21
Yang et al. 2024
Qwen2.5 Technical Report | Open-weight LLM
METHOD
• Open-weight language model family spanning roughly 0.5 to 72 billion parameters
• Large-scale pretraining followed by a long post-training stage for instructions
• Small variants explicitly targeted at resource-constrained deployment
• Reports structured-output and instruction-adherence benchmarks, not only knowledge
CONTRIBUTION
• A 1.5 billion parameter model small enough to fine-tune with LoRA on one GPU
• Open weights let the narration layer run entirely inside our own deployment
• Reliable structured output makes template-constrained narration feasible
• Small enough that the whole narration layer stays inside our own deployment
LIMITATION
• Text-only at the size we can afford, so it cannot look at an evidence crop
• Small models invent detail more readily than their larger siblings
• Cannot replace any part of the computer vision pipeline
HOW WE USE IT
• Base model for our LoRA narration experiment over incident cards
• Receives only the structured card fields as text, never the raw image
• Its invention risk is why narration is template-constrained and evidence-checked

## Slide 22
No single paper delivers the whole workflow
Each gap below is drawn from the survey, paired with the design decision it forced.
Gap in the literature | Where we saw it | Our design response
Alerts instead of records | Fang 2018 survey; Wu 2019 | Incident cards with worker, rule, time range and evidence crop
No identity or duration | Nath 2020; Luo 2018 | ByteTrack identities plus duration thresholds in rules
No visual evidence kept | Sanhudo 2021 | Best-frame crop stored with every incident for verification
No link to regulation | Fang 2018 survey | Retrieval-based briefing generated after the incident exists
Ungrounded explanation | Achiam 2023; Liu 2023 | Guardrail, evidence-overlap check, and refusal of legal verdicts

## Slide 23
Every component is measured on its own
This prevents a weak stage from hiding behind a convincing final demo.
Component | Metric | Evaluated on | Why this metric
Detection | mAP@50 and mAP@50-95 | Held-out site frames | Per-class, so small PPE objects cannot hide
Tracking | IDF1 and identity switches | Hand-checked worker tracks | Switches counted manually on short clips
PPE head | Macro-F1 and unknown rate | Held-out worker crops | A high unknown rate is acceptable, a wrong call is not
Rule engine | Incident precision and recall | Annotated clips | Scored against human-marked incidents
Language layer | Unsupported-claim rate | Generated briefings | Plus refusal rate on legal-verdict prompts
Usability | Time to understand one incident | New users | Measured on a first-time reviewer, not on us
No results are claimed at mid-review. This slide states what we will report and on which held-out data.

## Slide 24
Where we are and what comes next
IN ONE SENTENCE
Computer vision finds the incident and owns the evidence
The site view shows where it happened, and the language model explains it without ever deciding it.